## Slide 1: Leveraging on-hand motion sensors and 3d printed widgets to INTERACT WITH everyday things
07/06/2015

## Slide 2: Motivation/Intro
Opportunities
  Wearable devices are getting popular.
  Most smart watches, wristbands, rings have embedded motion sensors.

## Slide 3: Motivation/Intro
On Hand Motion Sensors
  Help transmitting hand motions, as well as hand sensory feelings to computers.
  E.g. Vibrations can be detected by accelerometers. Computers can learn more about the objects we are interacting with.

## Slide 4: Motivation/Intro
We explore how to leverage the power of on-hand motion sensors to interact with everyday things.

## Slide 5: Related Work
Interacting with physical objects (tangible interaction)
Acoustruments
Lamello

## Slide 6: Related Work
Interacting with everyday objects
MagicFinger
OmniTouch
Graspables
Portico

## Slide 7: Related Work - Three Challenges
Sensors might not be always available to ordinary objects.
The expression capability of hand gestures on physical objects is limited.
Improper installation of sensors on human body cause discomfort.
Notes: Installing the sensors might be very complex

## Slide 8: Our Work
using existing and emerging wearable devices in forms of watches and rings.
leveraging 3D printed widgets that can be easily attached to ordinary objects.
Sensors might not be always available to ordinary objects.
Improper installation of sensors on human body cause discomfort.
The expression capability of hand gestures on physical objects is limited.
Notes: Watches and rings are more acceptable to users.

## Slide 9: Benefits Brought by the Widgets
The system does not require extra electronic components to ordinary objects.
They are low-cost, and can be easily attached to ordinary objects.
They help providing identifiable touch signals. Common actions such as swiping, tapping, are enriched.
They provide passive tactile feedback. Users’ actions are more deterministic with them.

## Slide 10
Form factor | Pad Dial Pad Slider Button Scroll
Texture | 
Spacing | 
Shape | 
Height | 
Length | 
Uniformity | 
Direction | 

## Slide 11
Notes: This is the important part. Needs more efforts. Make a software to produce cad models for the widgets.

## Slide 12: Designing the widgets
How to design the widgets in the way that they can be attached to the other objects.
Make a guideline for designing such widgets.
Implement a software to produce 3d models of widgets.
Users can quickly make their own widgets for certain functions, and play with them.

## Slide 13: Recognition - Training
Step 1, 1.5s for users to perform actions
Step 2. Pick 32 frames
Chart: 
Chart: 
 | 0.04 | 0.08 | 0.02 | 0.1 | 0.3 | 0.25 | 0.29 | 0.36 | 0.43 | 0.39 | 0.38 | 0.26 | 0.57 | -0.19 | 0.09 | -0.1 | 0.09 | -0.49 | -0.41 | -0.49 | -0.55 | -0.06 | -0.48 | -0.84 | -0.86 | -0.97 | -0.17 | -0.28 | -0.14 | -0.25 | -0.09 | -0.03
 | -0.14 | -0.13 | -0.06 | -0.07 | -0.19 | -0.24 | -0.11 | -0.07 | 0.04 | -0.03 | 0 | -0.02 | 0 | -0.13 | 0.19 | -0.09 | -0.08 | -0.34 | 0.41 | 0.02 | -0.02 | 0.06 | -0.09 | 0.61 | 0.47 | -0.07 | 0.02 | -0.15 | -0.1 | -0.09 | -0.06 | 0.02
 | -0.05 | 0.08 | 0.03 | -0.02 | 0.24 | 0.09 | 0.21 | 0.2 | 0.04 | 0 | -0.11 | -0.08 | 0.19 | -0.07 | -0.27 | -0.19 | 0.36 | -0.17 | -0.25 | -0.07 | -0.05 | 0.33 | 0.57 | -0.18 | -0.31 | -0.16 | 0.35 | 0.51 | 0.34 | 0.12 | -0.18 | -0.22

## Slide 14: Recognition - Training
Step 3. Featurization
  Time Domain (4*3 + 2*4)
    { mean, std, skewness, kurtosis }, mean_std
  Frequency Domain (16*3)
    fft with 32 bins.
    sample number is 32, sampling rate is ~66Hz.
    each bin stands for 66/32 ~= 2.0625Hz
    the first 16 bins for (16 * 2.0625) ~= 33Hz
    signal over 33 Hz not being captured.

## Slide 15: Recognition
libSVM, with RBF(radial basis function / Gaussian) kernel.
Train with probability estimates.
Predict in real-time. 32 frames moving window, with 12 frames overlap.

## Slide 16: Recognition - Testing
Binary prediction (1, -1) has high accuracy (>98%)
Multi classes predictions, so far get accuracy rate around 80%.
Notes: 4-8-9 2-3-6 7

## Slide 17: Finds
Signals on wrist are weaker than the ones on fingers.
However, detection result shows no difference.
  E.g, for the pad
    82.4945% on wrist
    81.2819% on finger
  For keyboard
    >97% on wrist

## Slide 18: Finds
For the same gesture, accs responds differently.
Notes: Damp the vibrations. Need to test with different interaction context.

## Slide 19: Demo Applications

## Slide 20: Demo Applications

## Slide 21: Demo Applications

## Slide 22: User Evaluation
Human vs Sensors
  Can sensors be as good as humans for detecting vibration feedbacks.
Let users design their own widgets.
  With the software to design widgets, and to define interactions.
  We help them to make those widgets and let them play with them.